## Slide 1: Striving for SDR Performance Portability in the Era of Heterogeneous SoCs
Jeffrey S. Vetter
Seyong Lee
Mehmet Belviranli
Roberto Gioiosa
Richard Glassbrook
Abdel-Kareem Moadi
GNU Radio Conference 2019
Huntsville, Alabama
16 Sep 2019
ORNL is managed by UT-Battelle for the US Department of Energy
http://ft.ornl.gov vetter@computer.org

## Slide 2: Highlights
Motivation: Recent trends in computing paint an ambiguous future
  Contemporary systems provide evidence that power constraints are driving architectures to change rapidly
  Multiple architectural dimensions are being (dramatically) redesigned: Processors, node design, memory systems, I/O
  Complexity is our main challenge
Applications and software systems across many areas are all reaching a state of crisis
  Applications will not be functionally or performance portable across architectures
  Programming and operating systems need major redesign to address these architectural changes
  Procurements, acceptance testing, and operations of today’s new platforms depend on performance prediction and benchmarking.
ORNL Cosmic project investigating design and programming challenges for these trends in SDR
  Performance modeling and ontologies
  Performance portable compilation to many different heterogeneous architectures/SoCs
  Intelligent scheduling system to automate discovery, device selection, and data movement
  Targeting wide variety of existing and future architectures (DSSoC and others)

## Slide 3: Motivating Trends

## Slide 4: Contemporary devices are approaching fundamental limits
I.L. Markov, “Limits on fundamental limits to computation,” Nature, 512(7513):147-54, 2014, doi:10.1038/nature13570.
Economist, Mar 2016
R.H. Dennard, F.H. Gaensslen, V.L. Rideout, E. Bassous, and A.R. LeBlanc, “Design of ion-implanted MOSFET's with very small physical dimensions,” IEEE Journal of Solid-State Circuits, 9(5):256-68, 1974,
Dennard scaling has already ended. Dennard observed that voltage and current should be proportional to the linear dimensions of a transistor: 2x transistor count implies 40% faster and 50% more efficient.

## Slide 6: Business climate reflects this uncertainty, cost, complexity, consolidation

## Slide 7: Sixth Wave of Computing
http://www.kurzweilai.net/exponential-growth-of-computing
Transition Period
6th wave

## Slide 8: Predictions for Transition Period
Optimize Software and Expose New Hierarchical Parallelism
Use CMOS more effectively for specific workloads
Emerging Technologies
Investigate new computational paradigms
Quantum
Redesign software to boost performance on upcoming architectures
Neuromorphic
Advanced Digital
Architectural Specialization and Integration
Emerging Memory Devices
Integrate components to boost performance and eliminate inefficiencies
Exploit new levels of parallelism and efficient data movement
Workload specific memory+storage system design

## Slide 9: Predictions for Transition Period
Optimize Software and Expose New Hierarchical Parallelism
Use CMOS more effectively for specific workloads
Emerging Technologies
Investigate new computational paradigms
Quantum
Redesign software to boost performance on upcoming architectures
Neuromorphic
Advanced Digital
Architectural Specialization and Integration
Emerging Memory Devices
Integrate components to boost performance and eliminate inefficiencies
Exploit new levels of parallelism and efficient data movement
Workload specific memory+storage system design

## Slide 10: Predictions for Transition Period
Optimize Software and Expose New Hierarchical Parallelism
Use CMOS more effectively for specific workloads
Emerging Technologies
Investigate new computational paradigms
Quantum
Redesign software to boost performance on upcoming architectures
Neuromorphic
Advanced Digital
Architectural Specialization and Integration
Emerging Memory Devices
Integrate components to boost performance and eliminate inefficiencies
Exploit new levels of parallelism and efficient data movement
Workload specific memory+storage system design

## Slide 11: Quantum computing: Qubit design and fabrication have made recent progress but still face challenges
Science 354, 1091 (2016) – 2 December
http://nap.edu/25196

## Slide 12: Neuromorphic (Brain Inspired) Computing
SpiNNaker
IBM True North
BrainScaleS
DANNA
Others…
https://newsroom.intel.com/news/intels-pohoiki-beach-64-chip-neuromorphic-system-delivers-breakthrough-results-research-tests/
https://m-cacm.acm.org/news/201072-the-future-of-microchips

## Slide 13: New devices: Carbon Nanotube Transistors and Circuits
https://cen.acs.org/materials/electronic-materials/Carbon-nanotube-computers-face-makebreak/97/i8
https://spectrum.ieee.org/nanoclast/semiconductors/processors/modern-microprocessor-built-using-carbon-nanotubes

## Slide 14: Emerging Memory Devices
Image Source: IMEC

## Slide 15: Q: when was the field effect transistor patented?
https://www.edn.com/electronics-blogs/edn-moments/4422371/Lilienfeld-patents-field-effect-transistor--October-8--1926

## Slide 16: Predictions for Transition Period
Optimize Software and Expose New Hierarchical Parallelism
Use CMOS more effectively for specific workloads
Emerging Technologies
Investigate new computational paradigms
Quantum
Redesign software to boost performance on upcoming architectures
Neuromorphic
Advanced Digital
Architectural Specialization and Integration
Emerging Memory Devices
Integrate components to boost performance and eliminate inefficiencies
Exploit new levels of parallelism and efficient data movement
Workload specific memory+storage system design

## Slide 17: Pace of Architectural Specialization is Quickening
https://www.thebroadcastbridge.com/content/entry/1094/altera-announces-arria-10-2666mbps-ddr4-memory-fpga-interface
Industry, lacking Moore’s Law, will need to continue to differentiate products (to stay in business)
  Use the same transistors differently to enhance performance
Architectural design will become extremely important, critical
  Dark Silicon
  Address new parameters for benefits/curse of Moore’s Law
50+ new companies focusing on hardware for Machine Learning
http://www.wired.com/2016/05/google-tpu-custom-chips/
D.E. Shaw, M.M. Deneroff, R.O. Dror et al., “Anton, a special-purpose machine for molecular dynamics simulation,” Communications of the ACM, 51(7):91-7, 2008.
http://www.theinquirer.net/inquirer/news/2477796/intels-nervana-ai-platform-takes-aim-at-nvidias-gpu-techology
https://fossbytes.com/nvidia-volta-gddr6-2018/
Xilinx ACAP
HotChips 2018
HotChips 2018

## Slide 18: Future hardware will be far more diverse and mercurial than recent history (HotChips 2018)

## Slide 19: Analysis of Apple A-* SoCs
http://vlsiarch.eecs.harvard.edu/accelerators/die-photo-analysis

## Slide 20: Growing Open Source Hardware Movement Enables Rapid Chip Design
RISC-V Summit, 2018

## Slide 21: DARPA ERI Programs Aiming for Agile (and Frequent) Chip Creation
A. Olofsson, 2018

## Slide 22: Summary: Transition Period will be Disruptive – Opportunities and Pitfalls Abound
New devices and architectures may not be hidden in traditional levels of abstraction
Examples
  A new type of CNT transistor may be completely hidden from higher levels
  A new paradigm like quantum may require new architectures, programming models, and algorithmic approaches
Adapted from IEEE Rebooting Computing Chart

## Slide 23: Department of Energy (DOE) Roadmap to Exascale Systems An impressive, productive lineup of accelerated node systems supporting DOE’s mission
LLNL
IBM/NVIDIA
ANL
IBM BG/Q
ORNL
Cray/AMD/NVIDIA
LBNL
Cray/AMD/NVIDIA
LANL/SNL
TBD
ANL
Intel/Cray
ORNL
AMD/Cray
LLNL
TBD
LANL/SNL
Cray/Intel Xeon/KNL
2012
2016
2018
2020
2021-2023
ORNL
IBM/NVIDIA
LLNL
IBM BG/Q
Sequoia (10)
Cori (12)
Trinity (6)
Theta (24)
Mira (21)
Titan (9)
Summit (1)
NERSC-9
Perlmutter
Aurora
ANL
Cray/Intel KNL
LBNL
Cray/Intel Xeon/KNL
First U.S. Exascale Systems
Sierra (2)
Pre-Exascale Systems [Aggregate Linpack (Rmax) = 323 PF!]
Jan 2018
Heterogeneous Cores
Deep Memory incl NVM
Plateauing I/O Performance
Notes: Current pre-exascale systems (Rmax): 6.92 + 8.59 + 14.01 + 17.17 + 17.59 + 20.16 + 94.64 + 143.5

## Slide 25: Frontier: The OLCF 2021 Exascale computer
2021 delivery planned with >1000 PF performance (50–100 the scientific productivity of current Titan system)
Award contract
Design review
Prepare power, cooling, and space
Installation
CY 2017
CY 2018
CY 2019
CY 2020
CY 2021
CY 2022
CY 2023
Frontier NRE: hardware and software engineering
Prepare scientific software applications
Solicit bids for
computer build
Summit available: 200 PF production system
Frontier available
Titan available: 27 PF
Artificial intelligence
High- performance data analytics
Advanced simulations
http://procurement.ornl.gov/rfp/CORAL2/

## Slide 26: Frontier | 7 May 2019

## Slide 27: Final Report on Workshop on Extreme Heterogeneity
Maintaining and improving programmer productivity
  Flexible, expressive, programming models and languages
  Intelligent, domain-aware compilers and tools
  Composition of disparate software components
Managing resources intelligently
  Automated methods using introspection and machine learning
  Optimize for performance, energy efficiency, and availability
Modeling & predicting performance
  Evaluate impact of potential system designs and application mappings
  Model-automated optimization of applications
Enabling reproducible science despite non-determinism & asynchrony
  Methods for validation on non-deterministic architectures
  Detection and mitigation of pervasive faults and errors
Facilitating Data Management, Analytics, and Workflows
  Mapping of science workflows to heterogeneous hardware and software services
  Adapting workflows and services to meet facility-level objectives through learning approaches
https://orau.gov/exheterogeneity2018/
https://doi.org/10.2172/1473756

## Slide 28: The Summit System @ ORNL #1 on Top 500 since June 2018
Peak of 200 Petaflops (FP64) for modeling & simulation
Peak of 3.3 ExaOps (FP16) for data analytics and artificial intelligence
Max power 13 MW
  2 IBM POWER9 processors
  6 NVIDIA Tesla V100 GPUs
  608 GB of fast memory
    (96 GB HBM2 + 512 GB DDR4)
  1.6 TB of NV memory
  4,608 nodes
  Dual-rail Mellanox EDR InfiniBand network
  250 PB IBM file system transferring data at 2.5 TB/s
System Performance
Each node has
The system includes

## Slide 29: NVIDIA’s tesla v100
5,120 CUDA cores (64 on each of 80 SMs)
640 NEW Tensor cores (8 on each of 80 SMs)
20MB SM RF | 16MB Cache | 16GB HBM2 @ 900 GB/s
300 GB/s NVLink
7.5 FP64 TFLOPS | 15 FP32 TFLOPS | 120 Tensor TFLOPS
>27K of these on ORNL’s Summit system!
Mixed precision matrix math 4x4 matrices
The M&S community must figure how out to “cheat” and utilize mixed / reduced precisions
Ex: Jack Dongarra shows he can get 4x FP64 peak for 64bit LU on V100 with iterative mixed precision (using GMRES!)

## Slide 30: Frontier | 7 May 2019

## Slide 31: Department of Energy (DOE) Roadmap to Exascale Systems An impressive, productive lineup of accelerated node systems supporting DOE’s mission
LLNL
IBM/NVIDIA
ANL
IBM BG/Q
ORNL
Cray/AMD/NVIDIA
LBNL
Cray/AMD/NVIDIA
LANL/SNL
TBD
ANL
Intel/Cray
ORNL
AMD/Cray
LLNL
TBD
LANL/SNL
Cray/Intel Xeon/KNL
2012
2016
2018
2020
2021-2023
ORNL
IBM/NVIDIA
LLNL
IBM BG/Q
Sequoia (10)
Cori (12)
Trinity (6)
Theta (24)
Mira (21)
Titan (9)
Summit (1)
NERSC-9
Perlmutter
Aurora
ANL
Cray/Intel KNL
LBNL
Cray/Intel Xeon/KNL
First U.S. Exascale Systems
Sierra (2)
Pre-Exascale Systems [Aggregate Linpack (Rmax) = 323 PF!]
Jan 2018
Heterogeneous Cores
Deep Memory incl NVM
Plateauing I/O Performance
Notes: Current pre-exascale systems (Rmax): 6.92 + 8.59 + 14.01 + 17.17 + 17.59 + 20.16 + 94.64 + 143.5

## Slide 32: ORNL Cosmic Castle: Codesign for DSSoC Processors PY1.Q4 Review
Jeffrey S. Vetter
Seyong Lee
Mehmet Belviranli
Roberto Gioiosa
Richard Glassbrook
DARPA ERI DSSoC PY1Q4 Program Review
ORNL
17 Jul 2019
17 Jul 2019
DARPA ERI DSSoC Program: Dr. Tom Rondeau

## Slide 33: DARPA Domain-Specific System on a Chip (DSSoC) Program
DARPA ERI DSSoC Program: Dr. Tom Rondeau

## Slide 34: The history of GNU Radio inspiring the key technical areas of DSSoC
media.wired.com
www.ettus.com
www.mccdaq.com
2001
2004
2008
2013
2014
2015
commons.wikimedia.org
commons.wikimedia.org
commons.wikimedia.org
2008
commons.wikimedia.org
processors.wiki.ti.com
Moving to multi-core processors (i7)
Growing with technology (Pentium D)
Single core, single thread (Pentium 4)
Today
Processors
Computer
I/O
Intel
Arm
PowerPC
Server farms
Workstations
Laptops
Smart Phones
Embedded Systems
USB 2.0
USB 3.0
Thunderbolt2
1 GigE
10 GigE
PCIe x4
Multi-threaded scheduling (Cell Broadband Engine)
Embedded computing (Arm and Xilinx)
Introduction of VOLK
Porting to other SoCs
(TI Keystone II)
Porting to the smart phone (Android devices)
libvolk.org/
www.ti.com
Intelligent Scheduling Domain Representation MAC Software
Distribution Statement “A” (Approved for Public Release, Distribution Unlimited)
Slide courtesy of Dr. Tom Rondeau, DARPA MTO

## Slide 35: Getting the best out of specialization when we need programmability
DSSoC’s Full-Stack Integration
Application
Integrated performance analysis
Development Environment and Programming Languages
Libraries
Operating System
Compiler, linker, assembler
Intelligent scheduling/routing
Heterogeneous architecture composed of Processor Elements:
CPUs
Graphics processing units
Tensor product units
Neuromorphic units
Accelerators (e.g., FFT)
DSPs
Programmable logic
Math accelerators
Decoupled Software development
Hardware-Software Co-design
Medium Access Control
Looking at how Hardware/Software co-design is an enabler for efficient use of processing power
  Three Optimization Areas
    Design time
    Run time
    Compile time
Addressed via five program areas
  Intelligent scheduling
  Domain representations
  Software
  Medium access control (MAC)
  Hardware integration
Distribution Statement “A” (Approved for Public Release, Distribution Unlimited)
Slide courtesy of Dr. Tom Rondeau, DARPA MTO

## Slide 36: Domain-Specific System on Chip (DSSoC)
We cannot fully utilize our current multi-processor systems
We want to manage an increase of capabilities with integrated specialized accelerators
Programmed with different toolchains
Optimized to run a single application
Too general or application-specific
Intelligent tools to aid programmers
Domain-driven selection and layout
Simultaneously run multiple applications
Distribution Statement “A” (Approved for Public Release, Distribution Unlimited)
Slide courtesy of Dr. Tom Rondeau, DARPA MTO

## Slide 37: DSSoC: Domain-driven design
Distribution Statement “A” (Approved for Public Release, Distribution Unlimited)
Design: Processor Element selection and affinity analysis
Domain corpus
Literature, published text, code
Program Results
Domain ontology discovery
Development tools
(compilers, debuggers, performance analysis)
DSSoC
Design Space
38%
41%
3%
Design constraints
Workload mix
Acc
GPU
CPU
Acc
GPU
CPU
Acc
GPU
CPU
Intelligent
Scheduler
Compiler
Intermediate
Representation
(IR)
Ontology Generator
Performance counters
Percentage of ontology
Applications
e.g. GMTI, SAR, ESM
Performance monitor tools
Slide courtesy of Dr. Tom Rondeau, DARPA MTO

## Slide 38: Domain Specific System on Chip (DSSoC) Program to address these challenges Performer domains and applications
IBM T. J. Watson Research Center Pradip Bose
Columbia University, Harvard University, Univ. of Illinois at Urbana-Champaign
Arizona State University
Daniel W. Bliss
Univ. of Michigan, Carnegie Mellon University, General Dynamic Mission Systems, Arm Ltd., EpiSys Science
Stanford University
Mark Horowitz
Clark Barrett, Kayvon Fatahalian, Pat Hanrahan, Priyanka Raina
Oak Ridge National Laboratory
Jeffrey Vetter
CV+SDR
Multi-domain application
Multi-spectral processing
Communications
SDR
Unmanned aerial
Small robotic & leave-behind
Universal soldier systems
Multifunction systems
SDR
Communications and signal processing focused
Up-front processing / data cutdown
Improving understanding of processing systems
Computer Vision
  Still image and video processing
  Autonomous navigation
  Continuous surveillance
  Augmented reality
PlastyForma
IBM
Stanford
Google/YouTube
ORNL
Distribution Statement “A” (Approved for Public Release, Distribution Unlimited)
Slide courtesy of Dr. Tom Rondeau, DARPA MTO
Raytheon/Xilinx
Tom Kazior
SDR
Xilinx ACAP
Visual system integrator
Improved reconfigurability of processing systems
Raytheon

## Slide 39: ORNL Cosmic Castle
Contract Number: HR001117S0055--FP-008
Submission Date: Dec 2017
Review period: Feb 2019 – July 2019
Technical POC: Jeffrey S. Vetter, vetter@computer.org
Administrative POC: Richard Glassbrook, glassbrook@computer.org
Summary: Enabling codesign of DSSoC processors and software for mission-critical applications
Jeffrey Vetter, PI
Roberto Gioiosa, Runtime Systems
Mehmet Belviranli, Apps, Modeling, Ontologies
Seyong Lee, Programming Systems
Richard Glassbrook, Project Manager
Mohammad Monil, Intern, Oregon
Abdel-Kareem Moadi, Software/Hardware Engineer
Steve Moulton, Systems Engineer
Blaise Tine, Intern, Georgia Tech

## Slide 40: ORNL Cosmic Project
Jeffrey S. Vetter
Seyong Lee
Mehmet Belviranli
Roberto Gioiosa
Richard Glassbrook
Abdel-Kareem Moadi

## Slide 41: ORNL Cosmic Project

## Slide 42: Cosmic Castle | Development Lifecycle
Applications
Create scalable application Aspen models manually, with static or dynamic analysis, or using historical information
Ontologies
Ontologies based on Aspen models using statistical and machine learning techniques
Programming systems
Programming systems built to support ontologies
Runtime and Scheduling
DSSoC Chip
Query Aspen models and PFU for automatic code generation, optimization, etc.
Intelligent runtime scheduling uses models and PFU to inform dynamic decisions
DSSoC design quantitatively derived from application Aspen models
As feature of DSSoC, PFU API provides dynamic performance response of deployed DSSoC to intelligent runtime and programming system.
Performance Functional API
Dynamic resource discovery and monitoring
Early design space exploration with Aspen
Dynamic Performance Feedback including profiling and configuration response
Precise configuration and benchmark data for static analysis, mapping, partitioning, code generation, etc
DSSoC Design
DSSoC design quantitatively derived from application Aspen models
Early design space exploration with Aspen

## Slide 43: Cosmic Castle | Project Overview

## Slide 44: Project Overview

## Slide 45: Hardware

## Slide 46: Cosmic Castle | Project Overview

## Slide 48: Intel Stratix 10 FPGA available Experimental Computing Lab (ExCL) managed by the ORNL Future Technologies Group
Intel Stratix 10 FPGA and four banks of DDR4 external memory
  Board configuration: Nallatech 520 Network Acceleration Card
Up to 10 TFLOPS of peak single precision performance
25MBytes of L1 cache @ up to 94 TBytes/s peak bandwidth
2X Core performance gains over Arria® 10
Quartus and OpenCL software (Intel SDK v18.1) for using FPGA
Provide researcher access to advanced FPGA/SOC environment
https://excl.ornl.gov/
Mar 2019
For more information or to apply for an account, visit https://excl.ornl.gov/
Notes: Image source
https://www.intel.com/content/www/us/en/programmable/products/boards_and_kits/dev-kits/altera/kit-s10-fpga.html
https://www.nallatech.com/

## Slide 49: NVIDIA Jetson AGX Xavier SoC available Experimental Computing Lab (ExCL) managed by the ORNL Future Technologies Group
NVIDIA Jetson AGX Xavier:
High-performance system on a chip for autonomous machines
Heterogeneous SoC contains:
  Eight-core 64-bit ARMv8.2 CPU cluster (Carmel)
  1.4 CUDA TFLOPS (FP32) GPU with additional inference optimizations (Volta)
  11.4 DL TOPS (INT8) Deep learning accelerator (NVDLA)
  1.7 CV TOPS (INT8) 7-slot VLIW dual-processor Vision accelerator (PVA)
  A set of multimedia accelerators (stereo, LDC, optical flow)
Provides researchers access to advanced high-performance SOC environment
https://excl.ornl.gov/
Mar 2019
For more information or to apply for an account, visit https://excl.ornl.gov/
Notes: Image source
https://www.intel.com/content/www/us/en/programmable/products/boards_and_kits/dev-kits/altera/kit-s10-fpga.html
https://www.nallatech.com/

## Slide 50: Qualcomm 855 SoC (SM8510P) Experimental Computing Lab (ExCL) managed by the ORNL Future Technologies Group
Adreno 640
Hexagon 690
Kyro 485
Kyro 485 (8-ARM Prime+BigLittle Cores)
Prime
Core
Hexagon 690 (DSP + AI)
7nm TSMC
Adreno 640
Vulkan, OpenCL, OpenGL ES 3.1
Apps: HDR10+, HEVC, Dolby, etc
Enables 8k-360o VR video playback
20% faster compared to Adreno 630
Quad threaded Scalar Core
DSP + 4 Hexagon Vector Xccelerators
New Tensor Xccelerator for AI
Apps: AI, Voice Assistance, AV codecs
Snapdragon X24 LTE (855 built-in) modem LTE Category 20
Snapdragon X50 5G (external) modem (for 5G devices)
Qualcomm Wi-Fi 6-ready mobile platform: (802.11ax-ready, 802.11ac Wave 2, 802.11ay, 802.11ad)
Qualcomm 60 GHz Wi-Fi mobile platform: (802.11ay, 802.11ad)
Bluetooth Version: 5.0
Bluetooth Speed: 2 Mbps
High accuracy location with dual-frequency GNSS.
Connectivity (5G)
Spectra 360 ISP
New dedicated Image Signal Processor (ISP)
Dual 14-bit CV-ISPs; 48MP @ 30fps single camera
Hardware CV for object detection, tracking, streo depth process
6DoF XR Body tracking, H265, 4K60 HDR video capture, etc.
Spectra 360
5G
Qualcomm Development Board connected to (mcmurdo) HPZ820
Connected Qualcomm board to HPZ820 through USB
Development Environment: Android SDK/NDK
Login to mcmurdo machine
  $ ssh –Y mcmurdo
Setup Android platform tools and development environment
  $ source /home/nqx/setup_android.source
Run Hello-world on ARM cores
  $ git clone https://code.ornl.gov/nqx/helloworld-android
  $ make compile push run
Run OpenCL example on GPU
  $ git clone https://code.ornl.gov/nqx/opencl-img-processing
  Run Sobel edge detection
  $ make compile push run fetch
  Login to Qualcomm development board shell
  $ adb shell
  $ cd /data/local/tmp
Created by Narasinga Rao Miniskar, Steve Moulton
© Qualcomm Inc.
© Qualcomm Inc.
https://excl.ornl.gov/
For more information or to apply for an account, visit https://excl.ornl.gov/

## Slide 51: RISC-V

## Slide 52: Applications

## Slide 53: Applications

## Slide 54: End-to-End System: Gnu Radio for Wifi on two NVIDIA Xavier SoCs
Signal processing: An open-source implementation of IEEE-802.11 WIFI a/b/g with GNR OOT modules.
Input / Output file support via Socket PDU (UDP server) blocks
Image/Video transcoding with OpenCL/OpenCV
Video/Image Files
GNR IEEE-802.11 Transmit (TX)
UDP
Antenna
UDP
IEEE-802.11 Receive (RX)
Xavier SoC
Xavier SoC

## Slide 55: Applications Profiling
Preliminary SDR Application Profiling:
  Created fully automated GRC profiling toolkit
  Ran each of the 89 flowgraph for 30 seconds
  Profiled with performance counters
  Major overheads:
    Python glue code (libpython), O/S threading & profiling (kernel.kallsysms, libpthread), libc, ld, Qt
  Runtime overhead:
    Will require significant consideration when run on SoC
    Cannot be executed in parallel
    Hardware assisted scheduling is essential
Library | Percentage
[kernel.kallsyms] | 27.8547
libpython | 18.6281
libgnuradio | 11.7548
libc | 7.7503
ld | 3.8839
libvolk | 3.7963
libperl | 3.7837
[unknown] | 3.6465
libQt5 | 2.9866
libpthread | 2.1449
Chart: libgnuradio CPU-time Breakdown
| libgnuradio-analog | libgnuradio-blocks | libgnuradio-channels | libgnuradio-digital | libgnuradio-dtv | libgnuradio-fec | libgnuradio-fft | libgnuradio-filter | libgnuradio-pmt | libgnuradio-qtgui | libgnuradio-runtime | libgnuradio-trellis
 | 1.5501 | 0.72607 | 0.31562 | 0.49292 | 0.12281 | 1.1984 | 0.026966 | 0.89562 | 2.5055 | 0.13326 | 3.2931 | 0.49438

## Slide 56: GNR-Tools
GNR-Tools
  PY1Q2: Three tools are released
    Block-level Ontologies [ontologyAnalysis]
      Following properties are extracted from a batch of block definition files: Descriptions and IDs, source and sink ports (whether input/output is scalar, vector or multi-port), allowed data types, and additional algorithm-specific parameters
    Flowgraph Characterization [workflowAnalysis]
      Characterization of GNR workloads at the flowgraph level.
      Scripts automatically run for for 30 seconds and reports a breakdown of high-level library module calls
    Design-space Exploration [designSpaceCL]
      Script to run 13 blocks included in gr-clenabled - Both on a GPU and on a single CPU core - By using input sizes varying between 24 and 227 elements.
  PY1Q3: Two more tools are added
    cgran-scraper
    GRC-analyzer
https://code.ornl.gov/fub/gnr-tools

## Slide 57: New GNR-tools: cgran scraper and GRC statistics
cgran-scraper
  Scans all repos in cgran
  Automatically clones all repos
  Extracts all GRC files embedded within repos (currently xml formatted GRCs only)
GRC-analyzer
  Extracts two levels of static ontology information from a collection of GRC files
    Usage frequencies
    Block proximity graph
  Usage:
  Example:
    analyzeGRCXmls.py --grcFolder allGRCs --blockFilters sink source gui options note parameter variable import --mode proximityGraph

## Slide 58: GRC statistics: Block Usage Frequencies from CGRAN
Block usage frequencies
127 repositories, 641 GRC files
--mode usageFreq
Excluded filters: sink source gui options note parameter variable import pyqt
Duplicate occurrences of a block in a file removed
Highest 20 occurrences
Lowest 20 occurrences

## Slide 59: GRC statistics: Block Proximity Analysis
Block proximity analysis
Creates a graph:
  Nodes: Unique block types
  Edges: Blocks used in the same GRC file.
  Every co-occurrence increases edge weight by 1.
This example was run
  With --mode proximityGraph
  On randomly selected sub-set of GRC files

## Slide 60: GRC statistics: Block Proximity Analysis
Produces a GraphViz formatted dot file
  Can be visualized interactively by many open source tools
GEPHI: An open source tool that provides interactive layout & visualization
  Nodes are sized by degrees
  Edge weight determines thickness
  Selecting a node highlights co-occurrences
[Future] More analysis options:
  Nodes can be sized by frequencies
  Interactions can be filtered by GRCs
  Incorporate dynamic parameters

## Slide 61: Performance Modeling

## Slide 62: Integrating Modeling Across the Stack with Aspen

## Slide 63: Aspen: Abstract Scalable Performance Engineering Notation
Representation in Aspen
Modular
Sharable
Composable
Reflects prog structure
E.g., MD, UHPC CP 1, Lulesh,
3D FFT, CoMD, VPFFT, …
Source code
Aspen code
K. Spafford, et al, “Aspen: A Domain Specific Language for Performance Modeling,” in Proc. SC12.
Model Creation
Static analysis via compiler, tools
Empirical, Historical
Manual (for future applications)
Model Uses
Interactive tools for graphs, queries
Design space exploration
Workload Generation
Feedback to Runtime Systems

## Slide 64: GNURadio Flowgraph to Aspen Application Model Conversion
model blocks {
kernel complex_to_mag {
param aspen_param_default = 1
param aspen_param_sizeof_float = 4
param noutput_items = 8192
param aspen_param_sizeof_FComplex = 8
execute [noutput_items] "block_clComplexToMag_kernel4"
flops [1] as integer
execute "block_clComplexToMag_kernel4__intracommIN"
intracomm [(aspen_param_sizeof_FComplex*noutput_items)] as copyin
map [noutput_items] "mapblock_clComplexToMag_kernel4"
execute "block_clComplexToMag_kernel7" {
loads [(1*aspen_param_sizeof_FComplex)] as stride(1)
loads [(1*aspen_param_sizeof_FComplex)] as stride(1)
stores [(1*aspen_param_sizeof_float)] as stride(1)
flops [4] as dp, simd
}
execute "block_clComplexToMag_kernel4__intracommOUT"
intracomm [(aspen_param_sizeof_float*noutput_items)] as copyout
}
kernel complex_to_float {...}
...
}
    demod-uhd-sync.aspen
model demod-uhd-sync{
import uhd from "gr-uhd.aspen"
import blocks from "gr-blocks.aspen"
import digital from "gr-digital.aspen"
kernel main {
call uhd.usrp_source()
call blocks.multiply_const_vxx()
call digital.fll_band_edge_cc()
call digital.correlate_and_sync_cc()
parallel {
sequence{
parallel {
call blocks.complex_to_mag()
call blocks.complex_to_float()
}
call blocks_file_sink()
}
sequence{
call digital.pfb_clock_syc_xxx()
call digital.costas_loop_cc()
parallel {
call blocks.file_sink()
call blocks.file_sink()
}
}
}
}
}
    gr-blocks.aspen

## Slide 65: Block execution profiles on Xavier
Selected initial SoC: NVIDIA Xavier
  Volta GPU
  Octa-core ARM CPU
  Deep learning accelerator
  Vision Processor
Unique features of Xavier platform:
  First implementation of DLA arch.
  Detailed temperature and energy counters
  DVFS for both GPU and CPU
  Shared DDR memory (no global CC)

## Slide 66: Graph-Based Abstract Machine Model
class Zynq::Board-ZCU102 : Aspen::CompoundNode {
// Processing units
Zynq::APU cpu;
ARM::Mali400MP2 gpu;
ARM::CortexR5 rpu;
Xilinx::UltraScale+<nFPUs=400M> fpga;
// Memory
Aspen::DDR3<freq=2000MHZ, CL=16> systemMemory;
// Memory controllers, switchs, mmus
Zynq::SMMU smmu;
Aspen::Switch<bw=100GBs, latency= 25ns> lpSwitch;
Aspen::Switch<bw=1TBs, latency= 35ns> centralSwitch;
Aspen::PCIController<ver=3, totalLanes=24> pciController;
// Define interconnects (edges)
Aspen::Bus<bw=400GBps> cci_fp;
Aspen::Bus<bw=100GBps> cci_lp;
Aspen::PCIe<version=3,lane=16> pcieBus;
@add
cpu --cci_fp-- smmu;
gpu --cci_fp-- smmu;
fpga --cci_fp-- smmul
systemMemory --cci_fp[2]-- smmu; // Multiple links
smmu --cci_fp-- centralSwitch;
smmu --cci_fp-- pciController;
fpga --cci_fp[2]-- centralSwitch
lpSwitch --cci_fp-->> smmu; // Unidirectional link
lpSwitch <<--cci_fp-- centralSwitch
rpu --cci_lp[2]-- lpSwitch;
pciController --pcieBus -->> Aspen::OUTPUT
pciController <<--pcieBus -->> Aspen::INPUT
Nodes
Edges
Graph
Belviranli, M E, et al, "FLAME: Graph-based Hardware Representations for Rapid and Precise Performance Modeling", DATE'19

## Slide 67: Modeling Performance Behavior with Roofline
Roofline model sets an upper bound on performance of a kernel depending on the kernel’s operational intensity.
Plan [In progress]:
  Identify performance behavior of SDR modules
  Control arithmetic intensity by varying block sizes
  Create roofline-model for every architectural component
  Integrate the perf. model into graph-based machine model
Chart: GPU-OpenCL Speedup
| Math Op Const | Log10 | SNR Helper | Costas Loop | Complex Signal Source | Complex Conj | ComplexToMag | ComplexToMagAndPhase | ComplexToArg | MagPhaseToComplex | Quadrature Demod | Forward FFT | Reverse FFT
4 | 0.012821 | 0.0055249 | 0.018182 | 0.011494 | 0.015152 | 0.012821 | 0.016393 | 0.012821 | 0.015873 | 0.011236 | 0.011236 | 0.22917 | 0.27083
5 | 0.016949 | 0.012121 | 0.076923 | 0.055556 | 0.022727 | 0.016949 | 0.025641 | 0.017544 | 0.023256 | 0.011111 | 0.011364 | 0.30952 | 0.39394
6 | 0.018519 | 0.012903 | 0.12 | 0.096154 | 0.027027 | 0.018868 | 0.025641 | 0.019608 | 0.027778 | 0.010989 | 0.010638 | 0.34211 | 0.45455
7 | 0.018519 | 0.021505 | 0.31579 | 0.1875 | 0.025641 | 0.022222 | 0.02439 | 0.018182 | 0.025 | 0.034091 | 0.012048 | 0.36364 | 0.32353
8 | 0.018182 | 0.047101 | 0.52174 | 0.33333 | 0.046512 | 0.016667 | 0.025 | 0.066667 | 0.045455 | 0.034091 | 0.035714 | 0.36364 | 0.35294
9 | 0.017241 | 0.015696 | 1.3158 | 0.58065 | 0.054054 | 0.018868 | 0.02381 | 0.090909 | 0.11364 | 0.11494 | 0.08 | 0.36364 | 0.25714
10 | 0.033898 | 0.016908 | 1.75 | 1.1429 | 0.20455 | 0.041096 | 0.020833 | 0.18462 | 0.2 | 0.23 | 0.1215 | 0.34146 | 0.3617
11 | 0.066667 | 0.049853 | 2.8065 | 1.8596 | 0.4186 | 0.044776 | 0.045455 | 0.30303 | 0.30612 | 0.45977 | 0.2619 | 0.28571 | 0.25532
12 | 0.053333 | 0.051881 | 7.0741 | 2.4691 | 0.4375 | 0.10976 | 0.048387 | 0.55844 | 0.68421 | 0.39674 | 0.24719 | 0.48148 | 0.45455
13 | 0.15294 | 0.09319 | 7.5952 | 3.431 | 0.77465 | 0.19588 | 0.1039 | 0.7732 | 0.86517 | 0.40171 | 0.37931 | 0.63514 | 0.4382
14 | 0.23256 | 0.070896 | 13 | 4.8364 | 0.89286 | 0.25564 | 0.11 | 1.0956 | 1.4271 | 0.36999 | 0.27009 | 0.66116 | 0.59836
15 | 0.27143 | 0.050961 | 8.86 | 5.2045 | 1.526 | 0.37674 | 0.2406 | 1.4615 | 1.255 | 0.42655 | 0.2457 | 0.77457 | 0.67778

## Slide 68: Power profiles (stream on CPU/GPU sampled at 50ms)

## Slide 69: Block execution profiles on Xavier
Available HW counters in the Xavier platform (via Tegrastats application):
RAM 1903/15692MB (lfb 3251x4MB) 1903=Use of Ram, 15692=Total amount of RAM available, 4MB=Largest size of free block, 3251=Amount of free blocks of largest size
CPU [1%@1190,...,1%@1190] 1=Load statistics for each core, 1190=CPU freq in MHz
EMC_FREQ 17% 17=Percentage of bandwidth used relative to running frequency
GR3D_FREQ 0% 0=DGPU utilization
AO@32.5C Always on thermal zone temperature
GPU@32C GPU temperature
Tboard@32C Temperature inside external temperature sensor
Tdiode@34.75C External temperature sensor read through Tdoide inside TK1
AUX@31.5C Temperature of auxiliary sensor, located near CV cluster, SOC cluster
CPU@33.5C CPU Temperature
PMIC@100C Temperature of power management integrated circuit
GPU 0/10 0=Current GPU power consumption, 10=Average GPU power consumption
CPU 210/216 210=Current CPU power consumption, 216=Average CPU power consumption
SOC 860/864 860=Current System on Chip power consumption, 864=Average System on Chip power consumption
CV 0/0 140=Current PVA and DL power consumption, 144=Average PVA and DL power consumption
VDDRQ 140/144 140=Current DDR power consumption, 144=Average DDR power consumption
SYS5V 1880/1889 1880=Current system 5V power consumption, 1889=Average system 5V power consumption

## Slide 70: Block execution profiles on Xavier
Initial goal [In-progress]:
  Build complete GNR-block execution profiles
Per-block profiles:
  For every acceleratable GNR block
  On CPU, GPU and DLA
  For varying size of input sizes
SW challenges:
  Compile GNR, cl-enabled, CL-FFT and Volk
  No OpenCL support
    PoCL: Portable Computing Language
  DLA:
    Programmable via TensorRT
    Supports DL networks only as input
Device | Platform/SDK/API
OS/System | AArch64
Carmel Cores | ARM
Volta | CUDA / OpenACC
DLA | TensorRT
PVA | N/A (for now)

## Slide 71: Block execution profiles on Xavier
Research challenges [In-progress]:
  Shared DDR usage: capacity and contention concerns
  Energy / throughput / latency optimized co-location
  Low-overhead runtime monitoring for ARM cores
  Unified proxy/shim interfaces for universal profiling
  Analytical HW modeling of SoC and nested heterogeneity

## Slide 72: Programming Systems

## Slide 73: Programming Systems

## Slide 74: OpenARC: Open Accelerator Research Compiler*
OpenARC is the first open-sourced, OpenACC/OpenMP compiler supporting Altera FPGAs, in addition to NVIDIA/AMD GPUs and Intel Xeon Phis.
OpenARC is a high-level intermediate representation based, extensible compiler framework, where various performance optimizations, traceability mechanisms, fault tolerance techniques, etc., can be built for the complex heterogeneous computing.
* OpenARC, Lee, HPDC ‘14.

## Slide 75: Heterogeneous Architecture Support by OpenARC
Back End Compiler
Front End Compiler
CUDA
Nvidia GPUs
Xeon Phis
AMD GPUs
OpenACC/ OpenMP Program
Intel FPGAs
OpenCL
OpenCL
Intel OpenCL
DSSoCs
MCL
CPUs/Xeon Phis
OpenMP
OpenACC/OpenMP Interoperability

## Slide 76: Initial Performance of OpenACC GNU Radio Blocks on Xavier
Ported the OpenACC version of the GNU Radio blocks to OpenMP3 (CPU target), CUDA (GPU target), and OpenCL (GPU target) and compared against the reference CPU version.
Tested Platform: NVIDA Jetson Xavier (8-core ARM CPU, NVIDIA Volta GPU, two NVDLA Engines and VLIW Vision Processor)
Omitted MCL since JIT compilation not yet
factored
Notes: Consistent lower performance of the MCL version is due to JIT compilation overhead; if a target device is preselected before submitting to the MCL scheduler, the MCL task can be precompiled, which will have similar performance to other approaches.

## Slide 77: Program Characteristics Prediction of GNU Radio Blocks using Aspen
OpenARC automatically generates a structured Aspen performance model from the ported OpenACC code of the GNU Radio blocks.
Aspen performance prediction tools digest the generated Aspen models and derive performance predictions for the target application.
COMPASS: A Framework for Automated Performance Modeling and Prediction

## Slide 78: Initial Performance of OpenACC GNU Radio Blocks on Xavier (Cont.)
Ported the OpenACC version of the GNU Radio blocks to OpenMP3 (CPU target), CUDA (GPU target), OpenCL (GPU target), and MCL (GPU target) and compared against the reference CPU version.
  The reference CPU versions of accComplexToMagPhase and accComplexToMag blocks were vectorized with VOLK.
Tested Platform: NVIDA Jetson Xavier
CPU target: 8-core ARM CPU
GPU target: NVIDIA Volta GPU
Other targets: 2 NVDLA Engines and VLIW Vision Processor

## Slide 79: Intelligent Scheduler

## Slide 80: Programming Systems

## Slide 81: Cosmic Runtime and Scheduler
Framework for programming extremely heterogeneous systems
  Programming model and programming model runtime
  Maximize resource utilizations
  Abstract low-level architecture details from programmers
  Dynamically schedule work to available resources
Key programming features:
  Scheduler dispatches application tasks to available computing resources
  Asynchronous execution of runnable tasks
  Devices are managed by the scheduler and presented as “Processing Elements” to users
  Independent applications submit tasks without having to synchronize with each other
  Simplified APIs and programming model (e.g., compared to OpenCL)
Flexibility:
  Provides a scheduling framework in which new scheduling algorithm can be plugged in
  Multiple scheduling algorithms co-exist
  Users don’t need to port code when running on different systems
  Executing tasks on different PEs doesn’t require user intervention or code modification
  Resources allocated at the last moment
Submitted Tasks
IS
IS Interface
PEs
PFU Thread
IS Algorithm

## Slide 82: Exploiting Parallelism in SDR
Task Parallelism
Task
Task
Task
Task
Task
Pipelining
Data Parallelism
Application Parallelism
Notes: We need a new scheduler because most of the state-of-the-art solution focus on single application, just shared memory.
Resource sharing across different applications is typically done at OS level. Unfortunately, many OS don’t directly manage resources like GPUs or FPGAs
A side effects is that programs assume complete ownership of all resources -> select device 0 from platform 0 (e.g., Titan)

## Slide 83: Cosmic ISR / Prep
ISR assumes that user application …
  Written in high level, performance portable programming model (e.g., OpenACC or OpenCL if nec)
    OpenARC – presented in last section
  Has target code versions generated appropriate versions of target system code
    JIT is possible for OpenCL targets (except FPGA)
ISR contains specific RT modules for each device
ISR sets up dependencies as specified by compiler, user
ISR creates catalog of data to orchestrate data movement across disparate device memories

## Slide 84: Cosmic ISR / Execution
During execution, ISR must
  Discover available devices
  Pick the most appropriate device for the task
  Maintain dependencies
  Orchestrate data movement
Device selection uses any number of policies
  Random, Round-robin, profiling, hints, ontology, performance models (Aspen)
  ISR must also monitor existing device work to make tradeoffs
Current support for
  AMD GPU
  NVIDIA GPU
  CPU
  Xeon Phi
  Intel FPGA

## Slide 85: Introspective Layer
OpenCL provides a good compatibility layer but doesn’t provide sufficient introspective feedback:
  Performance counters
  Interference counters
  Power/Energy metrics
  Temperature sensors
ISR
Hardware
Application
OpenCL
ISR
Hardware
Application
OpenCL
ISR IL
OFI
ISR
Hardware
Application
ISR IL
OFI
ISR HAL

## Slide 86: The Minos Computing Library (MCL)
Framework for programming extremely heterogeneous systems
  Programming model and programming model runtime
  Maximize resource utilizations
  Abstract low-level architecture details from programmers
  Dynamically schedule work to available resources
Key programming features:
  Scheduler dispatches application tasks to available computing resources
  Asynchronous execution of runnable tasks
  Devices are managed by the scheduler and presented as “Processing Elements” to users
  Independent applications submit tasks without having to synchronize with each other
  Simplified APIs and programming model (e.g., compared to OpenCL)
Flexibility:
  Provides a scheduling framework in which new scheduling algorithm can be plugged in
  Multiple scheduling algorithms co-exist
  Users don’t need to port code when running on different systems
  Executing tasks on different PEs doesn’t require user intervention or code modification
  Resources allocated at the last moment

## Slide 87: IS Architecture 1/2
Multiple applications submit tasks
The IS algorithm dispatches each task to a PE
  Ontology-based performance expectations
  Contingent performance and power considerations
  PFU thread results
IS collects runtime introspective information
  System status
  Task execution characteristics (performance, power, occupancy, etc.)
  Estimates completion time
Submitted Tasks
IS
IS Interface
PEs
PFU Thread
IS Algorithm

## Slide 88: Platforms
System | CPU | GPU | Other
NVIDIA Jetson TX1 | 4-core ARM A57 | NVIDIA Maxwell | 
NVIDIA Xavier | 8-core ARM A57 | NVIDIA Volta | 2xDLMA
Xilinx ZCU 102 | 4-core ARM A53 | ARM Mali-400 MP2 | 2-core ARM R5
Apple iMac Pro | 16-core Intel Xeon | ATI Radeon Vega | 
GPU compute node | 2x 20-core Intel Xeon | NVIDIA Pascal | 
NVIDIA DGX1 P100 | 2x 20-core Intel Xeon | 8x NVIDIA Pascal | 
NVIDIA DGX1 V100 | 2x 20-core Intel Xeon | 4x NVIDIA Volta | Tensor cores
NVIDIA DGX1 V100 | 2x 20-core Intel Xeon | 8x NVIDIA Volta | Tensor cores
IBM Witherspoon | 2x 22-core IBM POWER9 | 6x NVIDIA Volta | Tensor cores
Currently ISR runs on a variety of architectures and systems
Time to port to a new system is 1 hour (mostly due to installing OpenCL libraries)
Same code runs out-of-the-box on new platforms

## Slide 89: Program Goal 1: System utilization
Target goal: 80%
Achieved goal: 95% sustained
Even with a simple round-robin resource load balancing and FIFO scheduler, MCL is effectively able to fully utilize the system, if there is enough work to be executed
Running 16k task of size 1024x1024 on a 8-GPU systems (NVIDIA Volta)
Leverage MCL internal tracing system
System utilization quickly climbs up and down during init/finit transient phases

## Slide 90: Program Goal 2: Concurrent applications
Target goal: 2
Achieved goal: N
MCL can run an unbounded number of independent applications and application processes, as long as there are available resources.
Running N applications on a 8-GPU systems (NVIDIA Volta)
Each applications runs 512 tasks
Tasks size starts from 2048x2048 to 64x64 (halved for each additional process)

## Slide 91: Resource-Based Waiting Time
Assume there is computing device with 100 Pes
Tasks arrived and are executed as long as there are available resources
If there are not enough resources, tasks are queued
Req: 50
Used: 0
Avail: 100
Req: 30
Used: 50
Avail: 50
Req: 20
Used: 80
Avail: 20
Used: 50
Avail: 50
Used: 30
Avail: 70
Req: 60
Used: 30
Avail: 70
Req: 60
Used: 100
Avail: 0
The waiting time of a task is computed between arrival time and expected time for required resources to be available

## Slide 92: Initial Results: Reference Ontology
We manually designed a reduced ontology for testing the Ontology-Based MCL scheduler v0.1
The application domain consists of:
  1 Application
  3 Different kernels (small, medium, large)
  3 Data structures (small, medium, large)
The reference SoC consists of:
  CPU cores (Intel Xeon)
  GPU cores (NVIDIA Volta) 2x
  DRAM memory
  GPU memory
Ontology generated with Protégé, stored in OWL
Evaluated 2 scenarios
1000 randomly generated kernels:
  Small and large kernels: probability 0.3
  Medium kernels: probability 0.4

## Slide 93: Experiment 1: Leveraging Slow Devices
Tested three different schedulers/policies:
All tasks set to MCL_TASK_ANY => tasks can run on any device
All tasks set to MCL_TASK_GPU => all tasks use the fastest device
Ontology-based scheduler
MCL ontology-based scheduler achieves higher performance by leveraging the CPU device when all GPU devices are busy

## Slide 94: Experiment 2: Waiting for Fast Devices
MCL ontology-based scheduler achieves higher performance by leveraging assigning tasks to GPU devices even if CPU devices are available

## Slide 95: Introspective Layer
OpenCL provides a good compatibility layer but doesn’t provide sufficient introspective feedback:
  Performance counters
  Interference counters
  Power/Energy metrics
  Temperature sensors
MCL
Hardware
Application
OpenCL
MCL
Hardware
Application
OpenCL
MCL IL
OFI
MCL
Hardware
Application
MCL IL
OFI
MCL HAL

## Slide 96: MCL + Aladdin
A pre-RTL, power- performance simulator designed to enable rapid design space search of accelerator-centric systems
The framework takes high-level language descriptions of algorithms as inputs, and uses dynamic data dependence graphs (DDDG) as a representation of an accelerator without having to generate RTL
Aladdin applies optimizations as well as constraints to the graph to create a realistic model of accelerator activity
Validate against RTL commercial tools
static void mvm(int *a, int *b, int *c,
int row, int col){
mvm: for (int i = 0; i < ROW; ++i){
c[i] = 0;
for(int j=0; j<COL; ++j){
c[i] += a[i*ROW+j] * b[j];
}
}
}

## Slide 97: Conclusions
MCL is progressing:
  Performance are getting better
  Larger set of tested architectures
  Additional kernels tested
  Integration with OpenARC compiler
Current Focus on first version of Ontology-based scheduler
  Based on manually-generated ontology
  Would provide better scheduling with additional knowledge in the ontology
Next steps:
  Hardware Abstraction Layer
  Introspective Layer
  Distributed MCL
  Execution on hardware different from CPU/GPU (e.g., DLMA, FPGA-based custom accelerators)

## Slide 98: Bonus

## Slide 99: Simple Execution Trace
Create
task
Set kernel
Set in/out
Submit task
Do more stuff
Do some more stuff
Check task
Select task
Exec
task
Dispatch task
Task completion
Task request
IS
App
PFU test
Load balance
Application
Scheduler
Worker thread
Contains introspective information
Contains resource information and constraints
Notes: Notice: the dispatched task is executed by a parallel worker thread, not the main thread

## Slide 100: MCL Performance: Performance
Tasks/kernels are small to highlight MCL overhead
Tasks/kernels executed on single GPU
MCL generally outperforms OpenCL
  Synchronous execution is similar to OpenCL execution model
  Asynchronous execution with 1 worker introduces some runtime overhead
  Asynchronous execution with M>1 workers outperforms OpenCL
    Hide data movement latency for small tasks (64x64) -> speedup up to 1.7x
    Efficient execution for larger tasks (1024x1024) -> speedup up to1.25x
GEMM kernel
64x64 with 4k tasks
1024x1024 with 512 tasks
Apple iMac Desktop Pro
1 ATI Radeon Pro Vega
  64 Cores
  8GB memory
1 Intel Xeon
  8 cores
  64 GB memory
MCL configuration
Synchronous 1 worker
Asynchronous 1,2,4,8 workers
Notes: Notice: these are “bad test”:
Very low computation
Meant to highlight scheduling and data transfer overheads

## Slide 101: Asynchronous Execution Engine
New engine expose a much higher level of parallelism
  Multiple workers VS internally parallel workers (backlog)
Even as few as 64 tasks (8 tasks/GPU), MCL achieves much higher performance than manual code
Need fewer tasks to saturate the system (about half)

## Slide 102: New Architecture: NVIDIA Xavier
System
NVIDIA Xavier
NVIDIA GPU (Volta) 512 cores
ARM Cortex A-57 8 cores
16GB HBM memory
GEMM kernel
1024x1024
Asynchronous execution
GPU Execution
Even with only on GPU, MCL achieves better performance:
Asynchronous execution
Internal concurrent workers

## Slide 103: MCL Performance: Use of all available resources – CPU+GPU
System
NVIDIA DGX1 P100
8 NVIDIA GPUs (Pascal)
  80 Cores, 192 threads/core
  16GB memory
2 Intel Xeon
  20 cores, 2 threads/core
  256GB memory
GEMM kernel
512x512*
16k tasks overall
Asynchronous execution
MCL can use all available resources at the same time
TASK_ANY
  Allows scheduler to decide which resource should be used for a task
On this system, GPUs are dramatically more power than CPUs
  Only 3% of the tasks execute on CPUs
  Performance is driven by GPU throughput
  This computation is well-suited for GPUs
* Task size has been reduced to fit both GPUs and CPUS
Notes: Current scheduler is simple: tasks get dispatched very quickly and wait in the queue of the device
Need to improve resource utilization: one tasked are dispatched they can’t be currently rescheduled <- modeling will help here

## Slide 104: MCL Ontology v0.1 (Xavier example)
The application domain consists of:
  3 Application
  6 Different kernels
  3 Data structures
The reference SoC consists of:
  CPU cores (ARM Cortex A57)
  GPU cores (NVIDIA Volta)
  NVIDIA DLMA
  DRAM memory
  GPU memory
  MemoryBus
  IOBus
Ontology generated with Protégé, stored in OWL

## Slide 105: Programmatic Highlights

## Slide 106: Outreach
IBM, Harvard, UIUC: initial discussions on programming systems, ontologies, simulation, SDR
Raytheon/Xilinx: FPGAs, RFNoC
Qualcomm: SDR hardware platform
GnuRadio Conference (Sep): Analysis tools and SDR on heterogeneous architectures
MODSIM Workshop (August): presentation on DSSoC and Cosmic Castle

## Slide 107: Summary

## Slide 108: Summary
Focus on end-to-end implementation of complete software/hardware scenario
Developed tools and identified scalable GNR workflow (WiFi)
Incrementally porting to heterogeneous programming model (OpenACC) to lower to multiple target programming models/architectures
MCL runtime scaling well on multiple platforms
Ontology
Use automated static and dynamic analysis tools to identify target GNR workflows suitable for acceleration
Programming Systems
Auto-compile identified applications to support accelerated execution
Intelligent Scheduling
Perform runtime resource management of the practical GNR-workflows
Hardware
Run the resources on the selected SoC with attached signal processing equipment
Applications
Create an end-to-end application scenarios that utilizes multiple processes in a pipeline
- “Find workflows that uses most amount of computation heavy GNR modules”
- GNR: IEEE-802.11 to transfer image and video files
- Transcoder: Convert content on the fly
- OpenARC generates MCL integrated OpenCL code and create corresponding GNR-OOT modules
- MCL runtime dynamically schedules kernels in GNR and transcoder processes
- NVIDIA Xavier: CPU/GPU/DLA
Ettus B210

## Slide 109: Cosmic-Castle Open Source Repositories
Step | Cosmic Castle’s Solution
1. Static/Dynamic GRC Workflow Analysis | Batch Processing for: Static analysis: Graph-based (.dot file) GRC workflow analysis Dynamic analysis: Automated profiling via perfmon Source: https://code.ornl.gov/fub/gnr-tools
2. Compiler framework | Source-code generation: OpenARC-based compiler-fronted automatically embeds MCL code for multi-device acceleration. Cosmic Castle GNR OOT modules are created to integrate the code into GNURadio. Source: https://code.ornl.gov/fub/gnr-cosmic
3. Applications & Toolchain | Toolchain: CC: Custom GRC files for TX/RX, python scripts for processing pipeline External:GNR OOT modules, OpenCL-based Image processing tools, dependencies etc. Source: https://code.ornl.gov/fub/cosmic-toolchain
4. Runtime Scheduler | Dynamic runtime for automated device selection and execution. Source: https://code.ornl.gov/r0g/Minos
5. Aspen modeling | Initial DSL modeling tools: https://github.com/ORNL/aspen

## Slide 110: Progress (since Feb 2019)
Continue development of tools to digest GNR framework, port modules to SoCs, identify bountiful modules, and refine ontologies to include performance and execution modalities
Partially created the OpenACC-enabled GNU Radio package, developed OpenACC/OpenMP interoperability feature, updated MCL backend support, and conducted initial performance portability tests and performance predictions of the ported OpenACC GNU Radio modules.
Ontology-based schedulers v0.1, continue porting on architectures (Xavier, Zynq, POWER9), asynchronous task engine optimizations, distributed execution, add additional functionalities for integration with OpenARC/ACC
Initial benchmarking of Xilinx Zynq and NVIDIA Xavier Jetson platforms.
Finish redesign of Aspen machine model for contemporary SoCs. Implement parser and symbol table to be coupled with application models.

## Slide 111: Conclusions
MCL is progressing:
  Performance are getting better
  Larger set of tested architectures
  Additional kernels tested
  Integration with OpenARC compiler
Current Focus on first version of Ontology-based scheduler
  Based on manually-generated ontology
  Would provide better scheduling with additional knowledge in the ontology
Next steps:
  Hardware Abstraction Layer
  Introspective Layer
  Distributed MCL (lower priority)
  Execution on hardware different from CPU/GPU (e.g., DLMA, FPGA-based custom accelerators)

## Slide 112: Conclusions
Domain Specific Systems on Chip (DSSoC)
  Developing software and architectures for specific domains
    SDR
  Heterogeneity by design
ORNL project
  SDR applications
  Targeting diverse array of heterogeneous hardware including upcoming chips
  Intelligent programming and runtime system
    OpenARC
    MCL
  Aspen models provides predictions for design, programming, and runtime decisions
Modeling and simulation challenges
  Clean slate chip design is too open
    Need hierarchy of models that allow early exploration through accurate design validation
  Performance prediction will be necessary to make compilation and scheduling intelligent

## Slide 113: Q&A

## Slide 114: Final Report on Workshop on Extreme Heterogeneity
Maintaining and improving programmer productivity
  Flexible, expressive, programming models and languages
  Intelligent, domain-aware compilers and tools
  Composition of disparate software components
Managing resources intelligently
  Automated methods using introspection and machine learning
  Optimize for performance, energy efficiency, and availability
Modeling & predicting performance
  Evaluate impact of potential system designs and application mappings
  Model-automated optimization of applications
Enabling reproducible science despite non-determinism & asynchrony
  Methods for validation on non-deterministic architectures
  Detection and mitigation of pervasive faults and errors
Facilitating Data Management, Analytics, and Workflows
  Mapping of science workflows to heterogeneous hardware and software services
  Adapting workflows and services to meet facility-level objectives through learning approaches
https://orau.gov/exheterogeneity2018/
https://doi.org/10.2172/1473756

## Slide 115: Recap
Motivation: Recent trends in computing paint an ambiguous future
  Multiple architectural dimensions are being (dramatically) redesigned: Processors, node design, memory systems, I/O
  Complexity is our main challenge
Applications and software systems across many areas are all reaching a state of crisis
  Need a focus on performance portability
ORNL Cosmic project investigating design and programming challenges for these trends in SDR
  Performance modeling and ontologies
  Performance portable compilation to many different heterogeneous architectures/SoCs
  Intelligent scheduling system to automate discovery, device selection, and data movement
  Targeting wide variety of existing and future architectures (DSSoC and others)
Visit us
  We host interns and other visitors year round
    Faculty, grad, undergrad, high school, industry
Jobs in FTG
  Postdoctoral Research Associate in Computer Science
  Software Engineer
  Computer Scientist
  Visit https://jobs.ornl.gov
Contact me vetter@ornl.gov

## Slide 116: Bonus Material

## Slide 117: ASCR Extreme Heterogeneity Workshop January 23-25, 2018 Virtual Meeting
Goal: Identify Priority Research Directions for Computer Science needed to make future supercomputers usable, useful and secure for science applications in the 2025-2040 timeframe
  Note that quantum computing was defined as out of scope by ASCR.
Primary focus on the software stack and programming models/environments/tools
150+ participants: DOE labs, academia, and industry
White papers solicited (106 received!) to contribute to the FSD, identify potential participants, and help refine the agenda
First ASCR workshop to use Basic Research Needs format (BES inspired)
  Summit, Summit report, Factual Status Document, whitepapers, BRN/PRD result
Organizing Committee
  Jeffrey Vetter (ORNL), Lead Organizer and Program Committee Chair
  Ron Brightwell (Sandia-NM), Pat McCormick (LANL), Rob Ross (ANL), John Shalf (LBNL)
  Lucy Nowell, ASCR Program Manager
Program Committee Members
  Katy Antypas (LBNL, NERSC), David Donofrio (LBNL), Maya Gokhale (LLNL), Travis Humble (ORNL), Catherine Schuman (ORNL), Brian Van Essen (LLNL), Shinjae Yoo (BNL)
https://orau.gov/exheterogeneity2018/
https://doi.org/10.2172/1473756

## Slide 118: Future Technologies Group (FTG) Jeffrey S. Vetter, Group Leader
NVIDIA Pascal
The Future Technologies Group performs research in core technologies for emerging generations of high-end computing architectures, including prototype computer architectures and experimental software systems. We investigate these technologies with the goal of improving the performance, energy efficiency, reliability, and productivity of these architectures for our sponsors and applications teams. See http://ft.ornl.gov.
Key Technical Areas
Heterogeneous architectures
Publications in SC, ICS, HPDC, TPDS, DATE, PLDI, IPDPS, Trans VLSI, etc.
Impact
Programming systems to address emerging architectures
Deep memory hierarchies including non-volatile memory
Performance measurement, analysis, simulation, and modeling of emerging architectures.
Software Artifacts
Beyond Moore's Computing
Scalable Heterogeneous Computing Benchmarks (SHOC)
mpiP
DESTINY
Aspen
OpenARC
Papyrus
NVL-C
Oxbow
LLVM Clacc and Parallel IR
Two Gordon Bell awards
NSF Keeneland
IEEE Fellows
DOE Titan
IEEE TCHPC Early Career
~100 interns
~130 FTG seminars
DRAGON
RISC-V Extensions
Sponsors
DOE ASCR, BER
DOE Exascale Computing Project
DARPA
ORNL LDRD
National Science Foundation
NIH
DOE SciDAC
Department of Defense
https://www.thebroadcastbridge.com/content/entry/1094/altera-announces-arria-10-2666mbps-ddr4-memory-fpga-interface
FusionIO

## Slide 119: Progression of Experimental Computing Technologies
CS & Math Research
TRL 1-3 Basic Concepts
TRL 7-9 Operational
TRL 4-6 Emerging
Examples: carbon-nanotube computing, memristor-based neuromorphic computing, chip-level silicon photonics, universal quantum computing
Examples: FPGAs in HPC, TrueNorth, SpiNNaker, D-Wave, Emu, many SoC-based systems, TPU, Gen-Z NoCs, near-memory computing
Examples: Titan, Cori, Mira, Summit, BlueWaters, Keeneland, Stampede, Tsubame2.5
Programming |  | Assembly language, or less |  | Few, if any, development tools |  | Language support and compilers.
OS-R |  | Manual |  | Specialized programming environments and OSs |  | Commodity OS & runtime systems
Scale |  | Small collections of devices |  | Single to hundreds of engineered processing elements |  | >10,000 processing elements
Performance |  | Analytical projections based on device empirical evaluation. |  | Analytical projections or simulation based on component or pilot system empirical evaluation. |  | Empirical evaluation of prototype and final systems.
Apps |  | Small encoded kernels |  | Architecture-aware algorithms; Mini-apps; Small applications |  | Numerical libraries; Full scale applications
Example |  | GPUs invented in 1999 |  | OpenGL in 2001; CUDA in 2007; OpenCL in 2008; OpenACC in 2010; DP in 2010; ECC in 2012 |  | GPUs are a fully supported compute technology in the HPC ecosystem.
Evaluate, Select, and Improve
Emerging Computing Technologies
“Bench” System
Limited Access Testbed
Experimental Prototype
Production

## Slide 120: ORNL ExCL Model
ExCL Common Infrastructure
Project and User management
Workshops
Shared Login and Gateway Nodes
Online discussions forums and issues
News
Authentication and Authorization
Shared Filesystems and Databases
Monitoring and control systems
Source Code and Data sets
Accounts
Projects and Proposals
Help
Community
Gateway nodes
Consistent and secure access to private network compartments
Secure operations
Partition access to specific compartments
System and account lifecycles
Data transfer nodes
Web
Source Code repos
Performance databases for applications and architectures
Manage privileged access levels
Manage access to shared resources
Lights out operation
Educational and reference materials
Outreach
Secure access to filesystems across pillars
Consolidated
Experience with management of export controlled and proprietary systems
Both Open and Controlled access
ExCL Technology Pillars
Data intensive: Emu
Quantum: Rigetti, IBM, D-wave
SoC: ThunderX2, Zynq
GPU: NVIDIA PASCAL, VOLTA
NVM: Intel Optane, Apache Pass
Neuromorphic: TrueNorth
FPGA: Intel Arria 10, Stratix 10, Xilinx U250
This year’s hot item
Deep memory: HBM2
Cloud: OpenStack Cluster
Cryogenic devices: JJ memory cell
Deep Learning
Per pillar expert collaboration
Pillars refreshed annually
https://excl.ornl.gov
Provide low-level access to emerging computer architectures to encourage experimentation and prototyping of new hardware and software solutions.
Not just testbeds, but staff and software environments to support this mode of operation.